## Slide 1
Compositional Monitoring of
Energy-Mix Drift on the Simplex
Peter Higgins
Independent researcher, Markham, Ontario, Canada
CoDaWork 2026 | Coimbra, Portugal | 1–5 June 2026

## Slide 2
The Problem
Monitoring ignores structure
Existing frameworks compare against external thresholds or models. None operate natively on the geometry of proportional allocation.
Energy mix is compositional
Shares of electricity generation by carrier sum to 100%. Arithmetic operations (differences, means) produce spurious results on such data.
Time has been overlooked
The CoDa community has rich cross-sectional tools. Formal time-series monitoring with perturbation-based drift measurement does not yet exist.

## Slide 3
The Protocol
1. Perturbation (compositional change)
Δ(t) = C( x₁(t+1)/x₁(t), …, x_D(t+1)/x_D(t) )
The compositional ratio between consecutive periods. Not arithmetic difference.
2. Aitchison Distance (drift magnitude)
d_A(x, y) = ‖ clr(x) − clr(y) ‖
The natural metric on the simplex. Invariant under perturbation and subcomposition.
3. Effective Diversity (concentration)
N_eff = exp( −Σ x_i ln(x_i) )
Equals D when all carriers contribute equally. Approaches 1 when one carrier dominates.

## Slide 4
Data
3
Countries
Germany, Japan, UK
9
Carriers
8-simplex
26
Years
2000–2025
Carriers: Coal · Gas · Nuclear · Hydro · Solar · Wind · Bioenergy · Other Fossil · Other Renewables
Source: EMBER Global Electricity Review (CC BY 4.0)
Zero replacement: multiplicative, δ = 10⁻⁶ (preserves ratios among non-zero parts)

## Slide 5
Germany
Nuclear Phase-Out and Energiewende

## Slide 6
Germany — Year-on-Year Aitchison Distance
Chart: 
| 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
d_A | 4.8189 | 0.7312 | 0.6555 | 0.5744 | 0.8092 | 0.5134 | 0.4552 | 3.2143 | 0.4604 | 0.5558 | 0.7791 | 0.4902 | 0.9251 | 0.3463 | 0.3706 | 0.367 | 0.322 | 0.2455 | 0.3675 | 0.3438 | 0.2716 | 0.7217 | 1.5336 | 9.0712 | 5.7331
Mean d_A = 1.3871 | σ = 2.0882 | Threshold (μ+2σ) = 5.5634 | Total shift from 2000: d_A = 17.85

## Slide 7
Germany — Drift Flags
2023 → 2024
d_A = 9.0712 (3.68σ above mean)
Final nuclear shutdown (April 2023) — full-year effect on composition. Nuclear: 1.4% → 0.0%
2024 → 2025
d_A = 5.7331 (2.08σ above mean)
Post-nuclear rebalancing continues. Coal, gas, solar, wind redistribute shares.
Effective Diversity
N_eff: 3.49 (2000) → 5.85 (2025)
Germany’s composition underwent a genuine regime change: 52% coal dominance in 2000 → distributed mix by 2025. Total structural shift d_A = 17.85 from baseline.

## Slide 8
Japan
Post-Fukushima Nuclear Withdrawal

## Slide 9
Japan — Year-on-Year Aitchison Distance
Chart: 
| 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
d_A | 0.8591 | 0.5064 | 0.7713 | 0.5886 | 0.3963 | 0.3181 | 0.3736 | 0.2135 | 0.5466 | 0.2875 | 0.8411 | 2.2063 | 0.6423 | 9.0477 | 7.846 | 1.3262 | 0.7688 | 0.5154 | 0.4687 | 0.5921 | 0.3502 | 0.4257 | 0.5569 | 0.3276
Mean d_A = 1.2823 | σ = 2.2043 | Threshold (μ+2σ) = 5.6909 | Total shift from 2000: d_A = 7.25

## Slide 10
Japan — Drift Flags
2013 → 2014
d_A = 9.0477 (3.52σ above mean)
Near-total nuclear shutdown. Nuclear fleet effectively offline; gas and coal absorb the burden.
2014 → 2015
d_A = 7.8460 (2.98σ above mean)
Nuclear output at zero for full year. Sharpest compositional shock in the dataset.
Effective Diversity
N_eff: 4.91 (2000) → 5.17 (2024)
Japan’s perturbation-based signal is unmistakable: a structural transition invisible to non-compositional methods that track absolute TWh rather than proportional reallocation.

## Slide 11
United Kingdom
Coal Exit

## Slide 12
United Kingdom — Year-on-Year Aitchison Distance
Chart: 
| 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
d_A | 0.349 | 0.295 | 0.4562 | 0.5527 | 2.9812 | 0.4073 | 0.3768 | 0.7326 | 0.4378 | 0.8336 | 1.7333 | 1.6899 | 0.5716 | 0.7712 | 0.6898 | 1.0458 | 0.4587 | 3.2263 | 0.8914 | 3.2579 | 0.3687 | 0.3076 | 0.4332 | 0.7091 | 1.7194
Mean d_A = 1.0118 | σ = 0.8945 | Threshold (μ+2σ) = 2.8008 | Total shift from 2000: d_A = 12.95

## Slide 13
United Kingdom — Drift Flags
2004 → 2005
d_A = 2.9812 (2.2σ above mean)
Dash-for-gas acceleration. Coal/gas ratio shifts sharply.
2017 → 2018
d_A = 3.2263 (2.48σ above mean)
Coal collapse phase accelerates. Coal share drops below 10%.
2019 → 2020
d_A = 3.2579 (2.51σ above mean)
COVID demand shock compounds coal near-zero. Coal: 1.8%.
Effective Diversity
N_eff: 3.71 (2000) → 5.24 (2025)
Steadiest structural drift of three countries: three flags spread over 15 years. Coal 31.8% (2000) → 0.1% (2025). Wind rises to 29.5%.

## Slide 14
Summary: Three Countries, Seven Flags
 | Germany | Japan | United Kingdom
Mean d_A | 1.3871 | 1.2823 | 1.0118
σ(d_A) | 2.0882 | 2.2043 | 0.8945
Max d_A | 9.0712 | 9.0477 | 3.2579
Flags | 2 | 2 | 3
Shift from 2000 | 17.85 | 7.25 | 12.95
N_eff trend | 3.49 → 5.85 | 4.91 → 5.17 | 3.71 → 5.24
Every drift flag corresponds to a documented energy-policy event.

## Slide 15
Open Question for the Community
Effective diversity N_eff = exp(H) and Aitchison norm ‖x‖_A = ‖clr(x)‖
Both quantify how “spread” a composition is across its parts. What is the formal relationship between these two measures? Under what conditions do they diverge? What does each reveal that the other does not?
The community’s expertise in simplex geometry may illuminate this connection.

## Slide 16
A Deeper Question
If we decimate a compositional time series —
compress 25 annual observations to 10, or 5 —
Which properties must the decimation
preserve to remain compositionally valid?
Empirical finding: Geometric-mean decimation preserves Shannon entropy to within 5%
across 35 NGFS scenario trajectories. Arithmetic decimation does not.
This suggests an entropy-invariance constraint on valid compositional
time-series operations — a constraint not yet formalised in the CoDa literature.

## Slide 17
Falsifiable Claim
No existing monitoring framework performs compositional change detection
at the carrier level with formal perturbation-based drift measurement.
Four ways to defeat this claim:
1. A published system using the Aitchison metric on energy-mix compositions
2. A published system measuring change as perturbation (compositional ratio)
3. A published system at individual carrier level within the simplex
4. A theoretical proof that CoDa adds no information beyond percentage monitoring
The author would welcome any of these outcomes. | All data, code, and documentation are publicly available.